## Slide 2
Everything You Always Wanted To Know About
Wi-Fi
Glenn R. Cate, N4GRC
May 4, 2018

## Slide 7: My Call Sign History
WN4NGW
WB4NGW
KA9FNL
KA9FNL/HI8
N4GRC

## Slide 8: My IT Certifications
CWNE #181
CWNA, CWAP, CWSP, CWDP
CompTia A+
Microsoft MCSE
Cisco CCNA
“I’m a ham!!”

## Slide 9: “Wi-Fi isn’t hard. How hard is it to not install wires?”

## Slide 10: Agenda
History of Wi-Fi
Wi-Fi in Our Lives
How Wi-Fi Works
Wi-Fi as a Career
Can you “Fix” My Wi-Fi?
Q&A

## Slide 12: It all Began with Hedy Lamarr
Austrian actress (1914-2000)
Co-invented with George Anthiel method to jam WWII Axis torpedoes
Used FHSS; part of legacy Wi-Fi and Bluetooth today
Notes: No, Hedy Lamarr did not “invent” FHSS (it was around before this time), but she did invent the usage for jamming Axis torpedes in WWII.
Technology not adopted by US Navy until the 1960s
FHSS was part of legacy Wi-Fi and is part of Bluetooth technology
Lamarr was inducted into the National Inventors Hall of Fame in 2014

## Slide 13: History of Wi-Fi
Wi-Fi does not mean “Wireless Fidelity”
  Interbrand was contracted by Wi-Fi Alliance (WFA) circa 1999 for brand creation
  Per WFA, “Wi-Fi doesn’t stand for anything.”
  WFA used tag line: “Standard for Wireless Fidelity”
  WFA approved “Wi-Fi” and the yin yang logo
  Wi-Fi (with hyphen)
Notes: WiFi Alliance wanted a term a bit catchier than “IEEE 802.11b Direct Sequence Spread Spectrum” and contracted Interbrand to come up with a better term.
For a while, WFA used tag line: “Wi-Fi: The Standard for Wireless Fidelity” but realized that was confusing things and was a mistake, so they dropped it.
Spell Wi-Fi as upper case W, lower case i, hyphen, upper case F, lower case i.

## Slide 15: OSI Layers
7. Application Layer
6. Presentation Layer
5. Session Layer
4. Transport Layer
3. Network Layer
2. Data Layer
1. Physical Layer (PHY)
Notes: IoT: door locks, refrigerators, HVAC and home A/C, wearable devices, security cameras, etc
“All People Seem To Need Data Processing”
Or…
“Please Do Not Throw Sausage Pizza Away”

## Slide 16: IEEE 802.11 PHY Standards
Protocol | Frequency | Signal | Date | Maximum data rate
Legacy 802.11 | 2.4 GHz | FHSS or DSSS | 1997 | 2 Mbps
802.11a | 5 GHz | OFDM | 1999 | 54 Mbps
802.11b | 2.4 GHz | HR-DSSS | 1999 | 11 Mbps
802.11g | 2.4 GHz | OFDM | 2003 | 54 Mbps
802.11n | 2.4 or 5 GHz | OFDM | 2009 | 600 Mbps
802.11ac | 5 GHz | 256-QAM | 2013 | 1.3 Gbps
802.11ax | 2.4 or 5 GHz | 1024-QAM | 2018 | 9.6 Gbps
Notes: 802.11 or 802.11 prime – 1997
802.11ax should be ratified by IEEE sometime this year (2018)

## Slide 17: Where is Wi-Fi Used Today?
Verticals (hospitals, airports, restaurants, offices, warehouses, retail, homes, etc.)
IoT (Internet of Things)
RTLS – location tracking
Outdoors (parking lots, parks, golf courses)
Point-to-Point (PtP) links
Everywhere!
Notes: IoT: door locks, refrigerators, HVAC and home A/C, wearable devices, security cameras, etc
RTLS: hospitals (track IV pumps and patients too); retail, theme parks

## Slide 18: DCF Arbitration
IEEE 802.11 standard
Wi-Fi is “polite” – uses half-duplex
So, how do 50 clients, all associated to the same AP and channel, take turns when they transmit?
Welcome to the DCF Arbitration Process!
Notes: IEEE 802.11 is the standard for Wi-Fi. Last revision has over 3500 pages!
DCF: Distributed Coordination Function
Wi-Fi is polite. Since it is half-duplex, it has to “take turns”
Roaming: Client makes roaming decision per the “secret sauce” of every AP manufacturer.

## Slide 19: DCF Arbitration
CSMA/CA (Carrier Sense Multiple Access-Collision Avoidance)
STAs use a physical carrier sense (Clear Channel Assessment—CCA) to determine if the WM is busy.
  ED (Energy Detect) – raw RF energy
  CS (Carrier Sense) – preamble detection in frame
Notes: 802.11 protocol (Wi-Fi) “avoids” collisions by using CSMA/CA
  Carrier Sense Multiple Access/Collision Avoidance
  802.3 (which is Ethernet) uses CSMA/CD (collision detection)
STA: any Wi-Fi station (client or AP)
WM = Wireless Medium
CCA has two components
  ED (Energy Detect) is listening for raw RF energy
  CS (Carrier Sense) is listening for “preamble detection” or listening only for the preamble of the 802.11 the wireless frame

## Slide 20: DCF Arbitration
STAs use a virtual carrier sense (Network Allocation Vector—NAV) to detect if the WM is busy. When the virtual timer (NAV) reaches zero, STAs may proceed
  Duration ID – value found in MAC frame header
  All STAs set their NAV timer to Duration ID of STA that is transmitting.
Notes: Virtual Carrier Sense uses NAV which has a timer that is set by using the duration ID values found in the MAC header of the frame
  Duration ID is the value in a frame that a station uses to tell others how long it takes for that STA to complete the conversation
NAV is the time each station hears from a transmitting STA in the Duration ID.
  All STAs then update

## Slide 21
Notes: IFS – Interframe Space (could be SIFS, DIFS, AIFS, PIFS or EIFS)
Most IFS lengths are 9 or 20 microseconds
Random backoff value – arbitrary and selected by each client
Keeps all STAs from transmitting at same time (if all NAVs = 0)

## Slide 22: Are You Interested in Wi-Fi as a Career?
Start with CWNP www.cwnp.com
Leading Wi-Fi vendors have online training (Cisco, Aruba, Aerohive, Ruckus, Mojo, etc.)
Wi-Fi blogs, webinars, YouTube, mentors
www.gcatewifi.wordpress.com for list of Wi-Fi blogs
Notes: CWNP is a great organization!
Next slide: The reason you all came out tonight—to get your Wi-Fi at home fixed!

## Slide 23: Can You Fix My Wi-Fi at Home?
The Need for Speed:
  Size and speed of your home ISP?
  This is usually the bottleneck
  Get at least 20/2 (DL/UL)
  Realize this is a “shared” internet circuit. Evenings and weekends are always busy!
Notes: Spectrum has default of 100/10 now, I think.
Get fastest you can as this is usually the bottleneck
WLAN engineers say “80% of wireless issues are client-related.”

## Slide 24: Can You Fix My Wi-Fi at Home?
Do you have Wi-Fi at home now?
  Is it an ISP provided AP? If so, they may have incorrect settings (more on this later)
  Be sure your AP (router) is in center of home
  If AP not provided, then buy one (Cisco-Linksys, Netgear, D-Link, TP-Link, Ubiquity, etc.)
  All have web page for setup (change admin pw!)
Notes: Your ”Router” at home is a multi-function device: It is an AP and firewall and switch and router, etc.
Wi-Fi at home:
  Incorrect settings by ISP
  AP in center of home, if possible (not in corner under pile of clothes)
  AP and NOT a “WAP”

## Slide 25: Can You Fix My Wi-Fi at Home?
“I have a big house and need more APs!”
  Cloud-based APs are good (Ubiquity, Open Mesh, Cisco Meraki are all good). Connected via Ethernet cables
  Mesh APs (Eero, Google Wi-Fi, Netgear Orbi)—they all “talk” to each other
  Use same SSID (network name) on all APs
Notes: Cisco Meraki – yearly/three-year subscription fee; these others do not.
Same SSID: You want to roam to the other AP, and the client always makes the roaming decision.

## Slide 26: Can You Fix My Wi-Fi at Home?
80% of Wi-Fi problems are client-related
  Check your WLAN NIC drivers (Windows, Android, Mac OS, iOS)
  Check your OS updates (Windows, Mac, Android)
  Changed password lately?
Notes: Drivers are probably the #1 item in this list!

## Slide 27: Can You Fix My Wi-Fi at Home?
Wi-Fi Settings (the ”correct” ones!)
  2.4 GHz: Only on channels, 1, 6 or 11
    Use a mobile app to see what channels are in use
    Be sure channel bonding is set to 20 MHz only!
  5.0 GHz: All channels are OK to use
    Use a mobile app to see what channels are in use
    Keep channel bonding to 40 or 80 MHz, not 160
Notes: 2.4 –ONLY use channels 1, 6 or 11 (unless you are in middle of Montana!)
Use 5 GHz if at all possible, especially in congested neighborhoods, apartments or condos

## Slide 28: 5 GHz Band (US Regulatory Domain)
Notes: UNII-1 and UNII-3 are always safe to use
UNII-2 and UNII-2 Ext are DFS channels – if detect radar, must change channel
  Near and around airports
  Near terminal doppler radar sites
  For home use, usually OK to use, but be aware channel may change

## Slide 29: Can You Fix My Wi-Fi at Home?
Wi-Fi Settings (the ”correct” ones!)
    Channel/power levels: suggest manual channels and power levels at 17 dBm (50 mW max). Use 14 dBm if you can.
    Data rates: If you can, disable (on 2.4 GHz) 1, 2, 5.5 and 11 Mbps rates, your network will run faster.
    Data rates: Check 5.0 GHz. OK to use, 6, 12 and 24 as basic rates.
    Leave all other settings as “default” (unless you know what you are doing)
Notes: Use “automatic” on channels in the 5 GHz band if there are a lot of other APs on this band.
Disable 1, 2, 5.5 and 11 – these are 11b rates (over 17 yr old technology). Eliminate protection mechanism and pm ripple
5 GHz: 6, 12, and 24 Mbps are usually the default settings

## Slide 30: Can You Fix My Wi-Fi at Home?
Wi-Fi Settings (the ”correct” ones!)
    SSIDs (network name): Use a simple one
      C or A or J. Not your last name or your dog, cat, etc.
      Setup a Guest SSID (call it G, not guest)
    Password: Use WPA2-PSK
      8 characters needed; pick something easy to remember
      Amat3ur! (8 characters: U.C., L.C., number, special character)
    Flash your router with latest firmware update
    If your router is “old”, buy a new one! (802.11ac device)
Notes: Firmware updates are done by looking in the web GUI on your router
New routers are $100 or less and will dramatically improve your home wireless network!
Recent ones on Amazon:
  TP-Link Archer AC1750: $59.99
  Netgear R6700 Nighthawk AC1750: $99.99
  Asus AC1900: $139.99
  Get an 802.11ac router (11n is older)

## Slide 31: Q & A ?
Notes: Slide deck will be up on the SPARC website

## Slide 32: TKS ES 73 DE N4GRC
@grcate
gcatewifi.wordpress.com
www.linkedin.com/in/grcate